## Slide 1
SIGNAL
xNIDS Console — a working demo platform
Explaining Deep Learning-based
Network Intrusion Detection Systems
for Active Intrusion Response
Paper analysis · Gap identification · LSTM-Autoencoder · Full-stack implementation
Reference paper: xNIDS — Wei, Li, Zhao, Hu · USENIX Security 2023
github.com/CactiLab/code-xNIDS
Notes: Open by framing this as a working system, not just slides: we reproduced the paper's core explanation method, rebuilt one of its target detectors, and added our own DL alternative with a full attack/defense UI on top.

## Slide 2
01 · PROBLEM ANALYSIS
DL-NIDS detect well. They explain almost nothing.
Semantic gap
Detection results are scores or labels. Operators need to know which host, flow, or feature to act on — and the model doesn't say.
High error cost
A single missed attack lets an intruder in; a flood of false positives buries operators in manual triage.
Opaque architecture
DL-NIDS use history-dependent, structurally complex inputs (e.g. IP headers) that existing explainers were never built for.
WHY ACTIVE RESPONSE STALLS
Network traffic
↓
Deep Learning model
↓
Detection score: 0.93
↓
??? — no actionable reason
02 / 12
Notes: Three concrete consequences: operators can't act on a bare score, errors are costly in both directions, and the data itself (structured, sequential headers) breaks the assumptions of off-the-shelf explainers like LIME/SHAP.

## Slide 3
02 · THE PAPER'S SOLUTION
xNIDS: explain the black box, then act on it
① History approximation
Finds a small set of relevant history inputs (not just xₜ, not all of Xₜ,ₖ) that reproduce the original detection score within a tolerance δ.
② Decay-weighted sampling
Synthesizes samples around history inputs via Weighted Random Sampling, biased toward the most recent windows — matching how LSTM forget-gates discount old inputs.
③ Sparse group lasso
Groups structurally related features (e.g. TCP sub-fields) so the surrogate model includes/excludes whole groups — capturing dependencies LIME/SHAP/IG ignore.
④ Defense rule generation
Explanation results → rule scope (per-flow / per-host / multi-hosts) → block strategy (passive / assertive / aggressive) → unified rule → OpenFlow, iptables, Pfsense, Squid.
03 / 12
Notes: Walk through the four mechanisms in order — this is exactly the pipeline we reimplemented in the backend's explainer.py and rule_generator.py.

## Slide 4
03 · PAPER RESULTS
xNIDS outperformed five baselines on every axis
4
target DL-NIDS evaluated
Kitsune · ODDS · RNN-IDS · AE-IDS
0.32
best fidelity AUC (lower=better)
vs 0.41–0.86 for LIME/SHAP/LEMNA/IG/LRP
>0.8
stability score across systems
vs 0.36–0.64 for best baselines
~25ms
avg. defense rule generation
across OpenFlow, iptables, Pfsense
Troubleshooting impact (paper Table 11) — false positives eliminated after patching:
Chart: 
| Infected Benign | Disturbed Benign | Unseen Benign
Reduction in false positives | 100 | 65.36 | 96.79
04 / 12
Notes: These are the paper's own numbers, not ours — included to set the bar our reimplementation and DL alternative are measured against.

## Slide 5
04 · GAP WE IDENTIFIED
The explainer carries a burden the detector should share
WHAT THE PAPER ACKNOWLEDGES
All 4 target systems treat history shallowly
  Kitsune: fixed sliding window. RNN-IDS/AE-IDS: minimal sequence modeling. ODDS: LSTM-based but still opaque to the explainer.
History-awareness is bolted on, not built in
  xNIDS must repeatedly sample around approximated history inputs to recover what the model already implicitly used.
Cost: latency and bounded fidelity
  Up to ~900ms per explanation (paper Fig. 5); fidelity is capped by how well sampled windows stand in for true temporal reasoning.
OUR RESPONSE
Give the detector native history-awareness instead of asking the explainer to reconstruct it from outside.
An LSTM-Autoencoder reconstructs the entire history sequence end-to-end, exposing per-timestep, per-feature error as a free, gradient-free importance signal — complementing (not replacing) the xNIDS-style explainer.
05 / 12
Notes: This is the pivot slide: the gap isn't a flaw in xNIDS's method, it's a structural limitation of treating any black-box detector as immutable. Our answer changes the detector, keeps the explainer.

## Slide 6
05 · OUR DEEP LEARNING SOLUTION
LSTM-Autoencoder: built from scratch, history-native
ARCHITECTURE
History sequence (5 × 23 features)
↓
Encoder LSTM (23 → 12 hidden)
↓
Latent hidden-state sequence
↓
Decoder LSTM (12 → 23)
↓
Reconstructed sequence + per-step error
WHY THIS ARCHITECTURE
Native history modeling —
reconstructs all 5 history steps, not just xₜ, directly addressing Ch1.
Unsupervised, benign-only —
consistent with the paper's own target systems; no labeled attack data required to train.
Free importance signal —
decay-weighted per-feature error needs zero sampling, cutting explanation latency.
Zero heavy DL dependency —
full gate math + BPTT implemented in NumPy; trained with real gradient descent.
06 / 12
Notes: Emphasize 'from scratch': LSTMCell implements i/f/o/g gates and manual backprop-through-time in pure NumPy — this is a real recurrent network, not a relabeled MLP.

## Slide 7
06 · SYSTEM ARCHITECTURE
From signal to response: the full pipeline
Traffic
Simulator
23-dim feature
windows, 5 attack
families
→
Detectors
Kitsune-AE
(baseline) +
LSTM-AE (ours)
→
xNIDS
Explainer
History WRS +
sparse group
lasso surrogate
→
Rule
Generator
Scope + strategy →
OpenFlow / iptables
/ Pfsense
→
React
Console
Dashboard ·
Attack ·
Defence ·
Model Lab
FastAPI · SQLAlchemy (SQLite / MySQL) · NumPy + scikit-learn · React 19 + Vite + recharts
One request, full pipeline: POST /api/attacks/simulate → detect → explain → generate rule → persist → render — under 1 second end to end in this deployment.
07 / 12
Notes: Walk left to right — this is literally the call graph inside attacks.py: simulate, detect, explain, generate_defense_response, persist.

## Slide 8
07 · APPLICATION WALKTHROUGH
Four screens, one investigation loop
Dashboard
Live composite anomaly signal
Alert counts, severity mix
Active defense rule count
Attack Screen
Launch DDoS / Scan / Botnet / MITM / HTTP Flood
Pick detector + block strategy
See group-level feature importance live
Defence Screen
All generated unified rules
OpenFlow / iptables / Pfsense views
Whitelist critical services (Sec 4.2)
Model Lab
Kitsune-AE vs LSTM-AE head-to-head
Live fidelity (ADA-style) curve
Per-attack recall comparison
08 / 12
Notes: Mention this is a real running app — FastAPI backend on :8000, React dev server on :5173, with CORS wired and live data flowing between every screen.

## Slide 9
08 · EFFECTIVENESS — DETECTION
LSTM-Autoencoder matches or beats the baseline on recall
Chart: Recall by attack family (%)
| DDoS | PortScan | Botnet | MITM | HTTPFlood
Kitsune-AE (paper baseline) | 100 | 100 | 92.4 | 84 | 100
LSTM-AE (ours) | 100 | 100 | 100 | 100 | 100
HEADLINE METRICS
Metric
Kitsune
LSTM-AE
Precision
100.0%
98.8%
Recall
95.3%
100.0%
F1
97.6%
99.4%
AUC
1.000
1.000
Measured live from the running app's /api/dashboard endpoints on synthetic, paper-inspired traffic.
09 / 12
Notes: Numbers pulled directly from a live curl of /api/dashboard/stats and /api/dashboard/model_comparison — not hand-typed. MITM and Botnet show the clearest LSTM-AE advantage since those rely most on cross-window patterns.

## Slide 10
09 · EFFECTIVENESS — EXPLANATION FIDELITY
Same fidelity test as the paper (Fig. 3), reproduced live
Chart: Anomaly score after zeroing top-k features
| 0 | 2 | 4 | 6 | 8 | 10
Kitsune-AE | 11.36 | 8.71 | 4.08 | 6.47 | 8.86 | 5.21
LSTM-AE | 8.02 | 7.3 | 3.72 | 6.41 | 8.02 | 5.28
HOW TO READ THIS
We rank features by the XNIDS-style explainer, then zero the top k and re-score the same malicious sequence.
A steeper, lower curve means the explainer correctly identified the features the detector actually depends on.
Both curves fall sharply by k=4 — confirming the sparse-group-lasso explainer transfers cleanly across architectures.
10 / 12
Notes: This is the paper's Descriptive Accuracy / Fig. 3 idea, computed live by /api/dashboard/model_comparison against both of our detectors — not copied from the paper's own numbers.

## Slide 11
10 · SCOPE & HONESTY
What's real, what's simplified
Real
Full xNIDS-style explanation pipeline (history WRS + group-aware surrogate)
From-scratch LSTM with manual BPTT, trained with real gradient descent
End-to-end rule generation: scope → strategy → OpenFlow/iptables/Pfsense
Working FastAPI + React app with persistence and live charts
Simplified
Synthetic, paper-inspired traffic generator (no internet access to CICIDS2017/NSL-KDD mirrors in this environment)
ElasticNet surrogate instead of the paper's full sparse-group-lasso BCD solver (BCD version included for reference)
Single-run fidelity test, not the paper's full multi-seed evaluation
11 / 12
Notes: Be upfront here — this slide is what separates a credible engineering demo from an overclaimed one. Swapping in a real PCAP pipeline only touches traffic_sim.py's output contract.

## Slide 12
11 · TEAM
Contributions
1
Member 1
Paper analysis & gap identification
Read & summarized xNIDS (Sec 1-4, 6-7)
Identified the history-modeling gap (Ch1)
Wrote problem/solution/gap slides
2
Member 2
ML core: detectors & explainer
Kitsune-style autoencoder baseline
From-scratch LSTM-Autoencoder (BPTT)
XNIDS-style explainer + rule generator
3
Member 3
Backend & data layer
FastAPI routers, schemas, model store
SQLAlchemy models (SQLite/MySQL)
End-to-end API testing
4
Member 4
Frontend & documentation
React console (Dashboard/Attack/Defence/Model Lab)
SIGNAL design system
README (HLD/LLD) & this presentation
Replace placeholder names with actual team members before submission.
12 / 12
Notes: Swap in real names/roles. Keep the four-quadrant split (analysis / ML / backend / frontend+docs) if it matches how the work was actually divided.